## Slide 1: Seven arm angles, three slalom courses, one score
Quadrotor: 0.829 kg · 5-inch props · 0.20 m arms · thrust/weight 5.24 · arms at ±t and 180° ± t from the forward axis
t = 20.44°
roll αφ 313.3
pitch αθ 120.8
t = 28.63°
roll αφ 233.1
pitch αθ 128.8
t = 36.81°
roll αφ 187.9
pitch αθ 140.9
t = 45.00°
roll αφ 159.9
pitch αθ 158.9
t = 53.19°
roll αφ 141.6
pitch αθ 186.3
t = 61.37°
roll αφ 129.3
pitch αθ 230.0
t = 69.56°
roll αφ 121.3
pitch αθ 305.7
narrow: stretched fore–aft, high roll authority
45° = classic X quad
wide: stretched laterally, high pitch authority
Authority = angular acceleration per newton of thrust (rad s⁻² N⁻¹), inertia-normalised. Roll authority varies 2.58× across the family; the weave is flown by banking.
Courses: same 2.4 m legs, sharper turn at every gate
θ = 60°
spacing 2.08 m · ±0.60 m
θ = 90°
spacing 1.70 m · ±0.85 m
θ = 120°
spacing 1.20 m · ±1.04 m
Six legs of each course, to scale; red bars are gates (0.5 m radius). Fixed leg length keeps every course 38.4 m long, so difficulty is not confounded with distance.
How an airframe is scored
Highest nominal speed at which all 15 gates are passed, found by bisection (±0.0625 m/s)
Pass: centre of mass within 0.5 m of the gate centre, in the gate plane, altitude included
Gains rederived per airframe (KR = ωn² I), so every body gets the same commanded bandwidth, 24 rad/s
Notes: The swept parameter is the arm half-angle t: low t stretches the frame fore-and-aft (high roll authority), high t stretches it laterally (high pitch authority); 45° is the classic X quad. The drone yaws to follow the path, so it weaves by banking and roll authority is the discriminating quantity. Courses differ only in the turn angle θ at each gate; leg length is fixed at 2.4 m so all courses are the same length. Score = maximum nominal speed that still passes every gate.

## Slide 2: The best arm angle depends on corner sharpness
Reduced model report Table 1 · no gyroscopic term
Corrected model report Table 3 · full rigid-body dynamics
t (°) | roll αφ | θ = 60° | θ = 90° | θ = 120°
20.44 | 313.3 | 9.891 | 7.977 | 6.648
28.63 | 233.0 | 10.086 | 8.289 | 6.609
36.81 | 187.9 | 10.164 | 8.367 | 6.531
45.00 | 159.9 | 10.164 | 8.250 | 6.414
53.19 | 141.6 | 10.164 | 8.172 | 6.297
61.37 | 129.3 | 10.125 | 8.016 | 6.219
69.56 | 121.3 | 9.930 | 7.859 | 6.180
spread across family |  | 2.7 % | 6.1 % | 7.1 %
t (°) | roll αφ | θ = 60° | θ = 90° | θ = 120°
20.44 | 313.3 | 10.086 | 5.555 | 5.281
28.63 | 233.0 | 10.242 | 6.297 | 6.375
36.81 | 187.9 | 10.398 | 6.961 | 6.219
45.00 | 159.9 | 10.203 | 8.250 | 6.688
53.19 | 141.6 | 10.047 | 8.172 | 7.078
61.37 | 129.3 | 9.969 | 8.133 | 7.078
69.56 | 121.3 | 10.008 | 8.211 | 7.117
spread across family |  | 4.1 % | 32.7 % | 25.8 %
Maximum completing speed (m/s). Orange = within the 0.0625 m/s bisection tolerance of the column best. Speeds are nominal (a difficulty scale): compare within a column only.
Optimum migrates to the narrow end as corners sharpen
θ = 60°
θ = 90°
θ = 120°
narrow 20.44°
wide 69.56°
Optimum migrates to the wide end as corners sharpen
θ = 60°
θ = 90°
θ = 120°
narrow 20.44°
wide 69.56°
Either way, no single static arm angle is best across the difficulty range — the case for morphing.
Which end wins sharp corners depends on the model: in the corrected one the narrowest frame drops to last, −32.7 % at 90° and −25.8 % at 120°, and the spread no longer grows monotonically with sharpness.
Notes: Reduced model: the optimum moves from a plateau at 36.81–61.37° (60°) to 36.81° (90°) to 20.44–28.63° (120°), and the spread grows 2.7 → 6.1 → 7.1 %. Corrected model (gyroscopic term integrated, quadratic yaw drag, idle-speed floor): 36.81° still wins at 60°, but 45/69.56° win at 90° and 53.19–69.56° at 120°. The 60° plateau is at bisection resolution. Nominal speed v sets T_total = T_startup + ℓ/v, so numbers are an ordinal scale, not physical gate speeds.

## Slide 3: Why the ranking flips: the yaw gyroscopic coupling
Only the yaw coupling depends on geometry
dΩz/dt = (Ixx − Iyy) / Izz · Ωx Ωy
−0.76
narrowest (20.44°)
0.00
X quad (45.00°)
+0.75
widest (69.56°)
Roll and pitch couplings are nearly the same on every frame (coefficients 0.92–0.99), since Izz ≈ Ixx + Iyy
The yaw coefficient changes sign across the family, on the axis the rotors control most weakly (yaw authority 6.43 vs 121–313 in roll)
Open: how the yaw torque turns into missed gates. Adding the coupling raises the narrow frame's sideslip at the gates (1.0° → 5.4° at 90°): a lead, not a result
Test: keep the term on one body axis at a time
θ | t (°) | no axis | roll | pitch | yaw | all
90° | 20.44 | 8.406 | 8.445 | 7.625 | 6.297 | 5.555
90° | 45.00 | 8.367 | 8.445 | 8.172 | 8.367 | 8.250
90° | 69.56 | 8.133 | 8.133 | 8.016 | 8.289 | 8.211
120° | 20.44 | 6.805 | 6.805 | 6.688 | 5.594 | 5.281
120° | 45.00 | 6.922 | 6.922 | 6.727 | 6.922 | 6.688
120° | 69.56 | 6.609 | 6.844 | 6.531 | 7.039 | 7.117
Maximum completing speed (m/s), report Table 4; “all” is the corrected model, “no axis” drops the term consistently.
Yaw alone reproduces 74 % / 79 % of the narrow frame's loss (90° / 120°) and 85 % of the wide frame's gain at 120°
With no coupling the narrowest frame ties the X quad at 90° and trails it at 120°: roll authority alone does not win the slalom
Implication
No static arm angle is best everywhere, which supports arms that sweep in flight. First, derive gains from the full inertia tensor: asymmetric sweeps break the mirror planes, and the diagonal form then misses its 24 rad/s target (22.4–26.0).
Notes: Every frame has the same Izz and Izz ≈ Ixx + Iyy, so roll and pitch gyroscopic accelerations are nearly identical across the family. Only the yaw coupling (Ixx − Iyy)/Izz · ΩxΩy depends on geometry: −0.76 on the narrowest frame, 0 on the X quad, +0.75 on the widest. Keeping the term on one axis at a time (plant and controller alike) attributes the narrow frame's loss mostly to yaw. The pathway from yaw torque to missed gates is not established: yaw saturation and heading lag were not confirmed on the corrected model. Caveats: one controller tuning (optimised on the X quad), one course per turn angle, mixer clips motors independently.